## Slide 1
2024 DSEATS DATATHON
13th July, 2024
Shedrach Igemhokhai, 5056696
SPE Benin section (Section 116)
Student, Dept. of Petroleum Engineering,
University of Benin.
A MACHINE LEARNING WORKFLOW FOR MULTIVARIATE PRODUCTION FORECASTING OF OIL AND GAS WELLS USING THE DSEAT FIELD DATA WITH WEB-BASED IMPLEMENTATION.

## Slide 2: OUTLINE
Introduction
Data Preparation
Exploratory Data Analysis (EDA)
Feature Engineering
Machine Learning Workflow
Web App Development
Conclusion and Future Work
Results
1
2
3
4
5
7
6
8

## Slide 3: INTRODUCTION
INPUT PARAMETERS
Utilize DSEAT field data to develop a stacked model for predicting oil, gas and water production rate.
METHODOLOGY
Implement best ML practices and evaluation techniques in obtaining best performing model
PERFORMANCE
Develop an effective generalizable model
WEB APP DEVELOPMENT
Develop a web app that implements workflow on new field data
Project Objectives
Production Forecasting involves predicting future production rates of oil, gas and water from reservoirs.
It is crucial for economics planning, investment decisions, reservoir management, and operational efficiency.
Traditional methods of production forecasting uses Decline Curve Analysis (Fig 1) and Material Balance, but this often assumes constant reservoir conditions and lacks flexibility.
Machine Learning can address this challenge by providing data-driven insights, adaptability to changing reservoir conditions and more accurate forecasts.
Combining ML with IoT and real-time data monitoring can enhance accuracy and efficiency.
Fig 1: A typical illustration of an oil and gas Decline Curve

## Slide 4: DATA PREPARATION
EXPLORATORY DATA ANALYSIS
Fig 2: Summary Statistics of historical data after cleaning procedures
The production data utilised in this project was acquired from the DSEATS field
For the dataset to be made suitable for use, it first needs to be cleaned
Missing values were removed, following standard machine learning practises
Upon inspection of the data, it contained negative production values. As this is not practically feasible, this very few roles were dropped
The data type was formatted, to ensure it is suitable for analysis and modelling
The DSEAT field contains a number of five different wells: DSEAT-001-F-12 H, DSEAT-001-F-14 H, DSEAT-001-F-11 H, DSEAT-001-F-15 D, and DSEAT-001-F-1 C , with production from 2008 to 2015
It consist of features ranging from date of production, average wellhead pressure to the produced reservoir fluids.

## Slide 5: EXPLORATORY DATA ANALYSIS - CONTD
Fig 3: Box plot of initial input features showing their distribution
Fig 4: Distribution plot of target features for well DSEAT-001-F-12 H
Fig 6: Oil production Cumulative density function plot for the different wells
Fig 5: Oil production decline curve for well DSEAT-001-F-12 H
Fig 7: Pairplot showing relationship between input features

## Slide 6: FEATURE ENGINEERING
The Pearson correlation heat map below in Fig 8 shows the relationship between the input features and the Targets.
The Engineered features show good relationship with the target. For instance, Days_From_Start show a high correlation of -0.72 with both oil and gas production rate.
An effective Machine learning model, depends significantly on the features utilized for training.
For most ML work, it is sometimes imperative to create new features that improves the effectiveness of the given models.
These features are often based on standard ML practises and domain knowledge
Fig 8: Pearson correlation coefficients between input and output parameters
Initial Features
Engineered Features
Targets

## Slide 7: MACHINE LEARNING WORKFLOW
Input
WHP
DHP
DHT
ATP
AP
CS
Pre-processing
Remove null values and dropped neg production values
Format Data types
Feature Engineering
CV Strategies
Grid Search
Cross Validation
Feature Scaling
Standard Scaling of data for non tree-based models
Machine Learning
Initialise Model
Optimise Model
Validate Model
Test Model
Forecasting
Output
Oil Rate
Gas Rate
Water Rate
Training and Test Splitting
Split data into 3 folds
Linear Regression
Kernel ridge regression
Random Forest
Xgboost
Gradient Boosting
Extra Trees
AdaBoost
MLP
80%
20%
The Workflow implemented in this project is shows in the process flow sideways.
The inputs are :
Average Wellhead Pressure(WHP)
Downhole Pressure (DHP)
Downhole Temperature (DHT)
Average Tubing Pressure (ATP)
Annulus Pressure (AP)
Choke Size (CS)
For all models, a Multi-Output approach was implemented, using a MutiOutputRegressor, whereby the individual models were trained and used to predict the production rates simultaneously.
Fig 9: Stacked model implementation
3 Fold Cross Validation
The best performing models were stacked together (fig 9) to form a meta-model. This meta-model has the advantage of generalization and reducing overfitting to the barest minimum.
Training
Test
Meta Model
Base Models
Data
Gradient Boost
Random Forest
XGboost
Extra Trees
Linear Regression
Final Predictions
Oil Rate
Gas Rate
Water Rate

## Slide 8: RESULTS
S/N | Model | (oil) | (gas) | (water) | MAE(oil) | MAE(gas) | MAE(water) | RMSE(oil) | RMSE(gas) | RMSE(water)
1 | Random Forest | 0.965 | 0.963 | 0.960 | 574.23 | 485806.55 | 880.14 | 1671.41 | 1356759.76 | 2355.40
2 | XGBoost | 0.963 | 0.959 | 0.958 | 657.40 | 562093.46 | 979.00 | 1704.09 | 1424948.95 | 2409.55
3 | Extra Trees | 0.969 | 0.968 | 0.963 | 504.96 | 431123.11 | 820.72 | 1570.87 | 1257968.43 | 2267.27
4 | Gradient Boosting | 0.954 | 0.952 | 0.955 | 807.77 | 676411.77 | 1032.28 | 1895.58 | 1546360.92 | 2500.41
5 | Stacked Model | 0.970 | 0.968 | 0.961 | 504.95 | 441146.38 | 887.88 | 1570.86 | 1269189.73 | 2333.86
S/N | Model |  |  |  | MAE(oil) | MAE(gas) | MAE(water) | RMSE(oil) | RMSE(gas) | RMSE(water)
1 | Random Forest | 0.965 | 0.963 | 0.960 | 574.23 | 485806.55 | 880.14 | 1671.41 | 1356759.76 | 2355.40
2 | XGBoost | 0.963 | 0.959 | 0.958 | 657.40 | 562093.46 | 979.00 | 1704.09 | 1424948.95 | 2409.55
3 | Extra Trees | 0.969 | 0.968 | 0.963 | 504.96 | 431123.11 | 820.72 | 1570.87 | 1257968.43 | 2267.27
4 | Gradient Boosting | 0.954 | 0.952 | 0.955 | 807.77 | 676411.77 | 1032.28 | 1895.58 | 1546360.92 | 2500.41
5 | Stacked Model | 0.970 | 0.968 | 0.961 | 504.95 | 441146.38 | 887.88 | 1570.86 | 1269189.73 | 2333.86
Actual oil rate
Predicted oil rate
Actual gas rate
Predicted gas rate
Actual water rate
Predicted water rate
Performance Evaluation of the five best models utilized in the workflow
Fig 10: oil rate predicted vs actual values
Fig 11: gas rate predicted vs actual values
Fig 12: water rate predicted vs actual values

## Slide 9: WEB APP DEVELOPMENT
RESULTS - CONTD
 | OIL (STB) | GAS (SCF) | WATER (STB)
HISTORY PERIOD | 58,896,759.06 | 48,411,804,354.70 | 79,757,652.20
FORECAST PERIOD | 28,236,170.49 | 24,468,848,461.62 | 20,244,097.03
TOTAL | 87,132,929.55 | 72,880,652,816.32 | 100,001,749.23
Total Production Estimation
Web app Development
Fig 13: Developed web app
For the Final Part of this project, The Machine Workflow was deployed in a local based-web app (fig 13). This web app would take the input data, and Perform the necessary data cleaning and feature engineering procedures and ultimately return the production forecasts and other valuable insights from the data.

## Slide 10: CONCLUSION AND FUTURE WORK
Contribution to Petroleum Industry
This work establishes an approach for applying machine learning to practical Oil and Gas problems
Possible Implementations
The result from this work can be adopted by engineers and economic analysts for accurate forecasting of production rates
Future Work
The methodology utilized can be applied to worldwide datasets to forecast reservoir production rates, and IoT can be implemented as well for real-time data monitoring and production rates forecasting
Limitations
A larger dataset encompassing different field from different geologic regions would have made the ML model more robust and generalizable
THANK YOU